## Slide 1: SMART TRAFFIC SYSTEM
PRESENTED BY
Priyanshu Sinha
Department of EEE, SILICON UNIVERSITY

## Slide 2: PROJECT OVERVIEW
Objective
To design & implement a Smart Traffic management System using IOT components to automate & optimise traffic control.
Key features:
RFID based vehicle identification
Ultrasonic sensor for vehicle detection
Vibration sensor for accident detection
Automated traffic lights
Real time control and alerts

## Slide 3: Components used
ESP32 Microcontroller: Core processing & Wi-fi connectivity.
RFID Module(MFRC522): Vehicle detection at traffic junction.
Traffic light LEDs & Relay Modules: Light control system
Power Supply & breadbroad: Circuit support & prototyping

## Slide 4: Working principle
RFID tags are detected at entry points to prioritize emergency or authorized vehicles.
Ultrasonic sensors detect vehicle density to dynamically change traffic light durations.
Vibration sensor identifies accidents & alerts control system.
ESP32 processes all inputs & controls lights via relays.
Data is processed & monitored using C++ & python code compiled using ARDUINO AI compiler.

## Slide 5: Programming details
Languages Used:
C++ for sensor interfacing and relay control
Platform: Arduino IDE
Features:
Modular code structure
Real time sensor polling
Dynamic LED control logic

## Slide 6: Results & Observations
Successfully detected vehicle presence using ultrasonic sensors
RFID based vehicle priority worked as expected
LEDs switched according to real-time traffic flow

## Slide 7
For Four Way system

## Slide 8
For Two Way system

## Slide 9
#include <SPI.h>
#include <MFRC522.h>
// RFID Pins
#define SS_PIN 5
#define RST_PIN 4
MFRC522 rfid(SS_PIN, RST_PIN);
// Traffic Light Pins
#define R1 25
#define Y1 26
#define G1 27
#define R2 14
#define Y2 12
#define G2 13
// Ultrasonic Sensor Pins
#define TRIG1 15
#define ECHO1 2
#define TRIG2 17
#define ECHO2 16
// Settings
const int vehicleThreshold = 10; // cm
int greenTime = 5000; // 5 seconds
int yellowTime = 3000; // 3 seconds
int allRedPause = 3000; // 3 seconds
void setup() {
Serial.begin(115200);
SPI.begin();
rfid.PCD_Init();
// Set pin modes
pinMode(TRIG1, OUTPUT); pinMode(ECHO1, INPUT);
pinMode(TRIG2, OUTPUT); pinMode(ECHO2, INPUT);
pinMode(R1, OUTPUT); pinMode(Y1, OUTPUT); pinMode(G1, OUTPUT);
pinMode(R2, OUTPUT); pinMode(Y2, OUTPUT); pinMode(G2, OUTPUT);
allRed();
Serial.println("🚦 Smart Traffic System Initialized");
}
void loop() {
// RFID Emergency Vehicle Detection
if (rfid.PICC_IsNewCardPresent() && rfid.PICC_ReadCardSerial()) {
if (isMasterCard()) {
Serial.println("🚨 Emergency Vehicle Detected → Road 1 Green");
greenLight(1, 20000);
allRed(); delay(2000);
} else {
String scannedUID = getUIDString();
Serial.print("Unknown RFID UID: ");
Serial.println(scannedUID);
}
rfid.PICC_HaltA();
return;
}
// Normal Traffic Cycle: Road 1
digitalWrite(R1, LOW); digitalWrite(G1, HIGH); digitalWrite(Y1, LOW);
digitalWrite(R2, HIGH); digitalWrite(G2, LOW); digitalWrite(Y2, LOW);
delay(greenTime);
digitalWrite(G1, LOW); digitalWrite(Y1, HIGH);
delay(yellowTime);
digitalWrite(Y1, LOW); digitalWrite(R1, HIGH);
delay(allRedPause);
// Road 2
digitalWrite(R2, LOW); digitalWrite(G2, HIGH); digitalWrite(Y2, LOW);
delay(greenTime);
digitalWrite(G2, LOW); digitalWrite(Y2, HIGH);
delay(yellowTime);
digitalWrite(Y2, LOW); digitalWrite(R2, HIGH);
delay(allRedPause);
// Check for vehicle presence
bool road1Busy = isVehicleConstantlyPresent(TRIG1, ECHO1);
bool road2Busy = isVehicleConstantlyPresent(TRIG2, ECHO2);
if (road1Busy) {
Serial.println("📈 Road 1 is busy → Extending Green");
greenLight(1, greenTime + 5000);
} else if (road2Busy) {
Serial.println("📈 Road 2 is busy → Extending Green");
greenLight(2, greenTime + 5000);
}
// Print distances
long distance1 = getDistance(TRIG1, ECHO1);
long distance2 = getDistance(TRIG2, ECHO2);
Serial.print("Distance on Road 1: ");
Serial.print((distance1 == -1) ? "Error" : String(distance1) + " cm");
Serial.print(" | Distance on Road 2: ");
Serial.println((distance2 == -1) ? "Error" : String(distance2) + " cm");
delay(1000);
}
// Get Distance from Ultrasonic Sensor
long getDistance(int trig, int echo) {
digitalWrite(trig, LOW);
delayMicroseconds(2);
digitalWrite(trig, HIGH);
delayMicroseconds(10);
digitalWrite(trig, LOW);
long duration = pulseIn(echo, HIGH, 30000); // timeout 30ms
if (duration == 0) return -1;
return duration * 0.0343 / 2;
}
// Check if vehicle consistently present
bool isVehicleConstantlyPresent(int trig, int echo) {
int count = 0;
for (int i = 0; i < 5; i++) {
long d = getDistance(trig, echo);
if (d > 0 && d < vehicleThreshold) count++;
delay(200);
}
return count >= 4; // majority detected
}
// Convert UID to String
String getUIDString() {
String content = "";
for (byte i = 0; i < rfid.uid.size; i++) {
if (rfid.uid.uidByte[i] < 0x10) content += "0";
content += String(rfid.uid.uidByte[i], HEX);
if (i < rfid.uid.size - 1) content += " ";
}
content.toUpperCase();
return content;
}
// Check if Scanned UID Matches Emergency UID
bool isMasterCard() {
String uidStr = getUIDString();
Serial.print("Scanned UID: ");
Serial.println(uidStr);
return (uidStr == "83 22 29 3"); // Replace with your actual emergency UID
}
// Give green light to specified road
void greenLight(int road, int duration) {
if (road == 1) {
digitalWrite(G2, LOW); digitalWrite(Y2, HIGH);
delay(2000);
digitalWrite(Y2, LOW); digitalWrite(R2, HIGH);
digitalWrite(R1, LOW); digitalWrite(G1, HIGH);
} else {
digitalWrite(G1, LOW); digitalWrite(Y1, HIGH);
delay(2000);
digitalWrite(Y1, LOW); digitalWrite(R1, HIGH);
digitalWrite(R2, LOW); digitalWrite(G2, HIGH);
}
delay(duration);
digitalWrite(G1, LOW); digitalWrite(G2, LOW);
}
// Turn all lights to red
void allRed() {
digitalWrite(R1, HIGH); digitalWrite(Y1, LOW); digitalWrite(G1, LOW);
digitalWrite(R2, HIGH); digitalWrite(Y2, LOW); digitalWrite(G2, LOW);
}

## Slide 10: Applications
Smart city traffic management
Emergency vehicle prioritization
Accident detection & reporting
Scalable for multiple junctions

## Slide 11: Future enhancements
Integration with cloud for remote monitoring
GPS module for vehicle plate detection
Mobile app integration
Camera module for license plate detection

## Slide 12: CONCLUSION
Implemented a functional smart traffic system using IOT & ESP32
Achieved real time traffic sensing & control
Project combines embedded systems with AI compiled logic